Cadillac ATS Climate Control set for 72º; Auto AC; Mode = Upper

G35 Climate Control set for 71°;  Auto AC; Mode = Upper

| Date | Time | Outside Temp | Driver Temp | Passenger Temp | Comments |
| --- | --- | --- | --- | --- | --- |
| 8/29 | 1002 | n/a | 45 | 46 | Cadillac ATS used for comparison |
| 8/29 | 1121 | 88 | 43 | 44 | Air to cabin comes in @ 43 - 46 degrees |
| 9/2 | 0952 | 78 | 61 | 59 | 18 min run. Outside temp moderate |
| 9/2 | 1010 | 78 | 72 | 63 | Driver temp levels off @ 72° |
| 9/2 | 1010 | 78 | 72 | 62 | Pass temp levels @ approx. 60° |
| 9/2 | 1016 | 80 | 66 | 61 | 2 min run. Outside temp moderate. |
| 9/2 | 1017 | 80 | 71 | 61 | Approx 10° diff between driver and passenger |
| 9/4 | 1451 | 100 | 100 | 103 | 14 min run. Outside air very hot. |
| 9/4 | 1458 | 89 | 85 | 71 | After 7 min, D&P 14° diff. After 14 min, |
| 9/4 | 1505 | 89 | 80 | 69 | After 14 min, D&P approx 11° diff, 11° diff |
| 9/5 | 1401 | 90 | 87 | 73 | 2 min run. Outside temp hot. |
| 9/5 | 1402 | 90 | 85 | 71 | Driver slow pulling down, Passenger quicker |
| 9/5 | 1402 | 90 | 84 | 70 | Approx 14° diff w/ Passenger only 70° |
| 9/5 | 1452 | 91 | 100 | 105 | 14 min run. Outside air hot. Cab very hot. |
| 9/5 | 1454 | 91 | 96 | 81 | After 2 min, D&P approx 15° diff |
| 9/5 | 1455 | 92 | 98 | 77 | After 4 min only Passenger pulling down (21° diff) |
| 9/5 | 1456 | 92 | 93 | 77 | After 4 min , D&P approx 16° diff |
| 9/5 | 1457 | 92 | 95 | 75 | After 5 min , D&P approx 20° diff |
| 9/5 | 1458 | 92 | 94 | 75 | After 6 min , D&P approx 19° diff |
| 9/5 | 1502 | 93 | 92 | 74 | After 10 min , D&P approx 18° diff |
| 9/5 | 1502 | 93 | 92 | 74 | After 10 min , D&P approx 18° diff |
| 9/5 | 1502 | 92 | 89 | 73 | After 10 1/2 min , D&P approx 16° diff |
| 9/5 | 1506 | 92 | 89 | 73 | After 14 min neither side pulled down enough. |
| 9/8 | 1843 | 84 | 65 | 60 | 17 min run. Outside air moderate, cab fairly cool |
| 9/8 | 1847 | 86 | 60 | 59 | After 4 min , D&P approx same |
| 9/8 | 1900 | 84 | 58 | 58 | After 17 min D&P same but a max cool of 58° |
| 9/21 | 1349 | 84 | 86 | 87 | 23 minute run. Outside temp moderate. |
| 9/21 | 1412 | 86 | 61 | 59 | Both sides come down to approx 60° |
| 9/24 | 1709 | 84 | 97 | 100 | 11 min run. Hot day, cab temps approx.100° |
| 9/24 | 1720 | 86 | 66 | 63 | Driver lagging passenger cooling w/ max of 63° |
| 9/27 | 1401 | 81 | 84 | 87 | 5 min run. Moderate outside temp. |
| 9/27 | 1406 | 81 | 58 | 59 | Both sides cool down quickly, but not under 58° |
| 9/27 | 1442 | 83 | 81 | 81 | 15 min run. Moderate outside temp. |
| 9/27 | 1457 | 81 | 59 | 59 | Both sides cool down but not under 59° |
| 10/01 | 1527 | 84 | 90 | 94 | 16 min run. Moderate outside temp. |
| 10/01 | 1543 | 80 | 53 | 52 | Both side cool down but still 52° is lowest it gets |
| 10/01 | 1552 | 80 | 64 | 66 | 5 min. run Car cool from last run. Outside cool |
| 10/01 | 1557 | 80 | 56 | 54 | Both sides cool but 54° is lowest it got. |
| 10/02 | 1519 | 84 | 90 | 94 | 7 min run. Outside temp moderate. |
| 10/02 | 1523 | 84 | 80 | 68 | Driver side resisting and lags Passenger side by |
| 10/02 | 1526 | 84 | 79 | 67 | 12° differential |

NOTE: Runs are recorded with alternate white and grey shading.

My Observations

- The lowest temperature of cooled air entering the cabin is only 58°. The Cadillac cooling air entering the cabin comes in at approx. 45° and did go down to 43° in the second test performed.

- On very hot days the Driver side cool air temp most times will not go below 80°, and the Passenger side not below 70°. As they are cooling down there is a big differential between the two temperatures. I do not know if the normal path of cooling air after it leaves the evaporator feeds the Passenger side ducts first and then flows to the Driver side ducts which would explain the differential, or since they do have dual temperature zone options if there is a baffle between them that is causing a problem.

- In addition to the differential between the D & P cooling air the lowest temperature air that the AC seems capable of supplying is 53°. Even if the climate control is functioning properly, the ac unit doesn’t seem to be able to satisfy the demand.

- On relatively cooler days both sides do come down fairly even to supply cool air at about 58° to 60°, but that is supply air, the cabin temperature barely reaches a comfortable level.

- I think we need to establish that the ac unit is capable of supplying air between 40° to 50° as any new ac unit should be able to do. Then we need find out why there is a differential between the two sides also. I placed the OEM climate control unit in the trunk in case it is needed.