Filter Efficiency and Dust Pass Through

Even though efficiency is reported as the percentage of dust a filter collects, true efficiency is more about what is allowed to pass through a filter rather than what is stopped by it. It is the dust passing through a filter that causes engine damage and premature wear and failure.

When looking at collection efficiency, it is easy to overlook the differences in the volume of dust going through a filter of 99% efficiency versus a filter that’s 99.5% efficient. The 0.5% difference seems insignificant until you realize that the 99% filter allows 2 times more dust to pass through than the 99.5% filter.

Following is a list of some of the popular 14” round filters we tested and the increase in dust volumes they allow over an R2C filter:

Filter		Efficiency		Multiples more dust pass through

R2C		99.7%			0

Green		93.6%			21.33 times more dust

AEM		97.5%			8.33 times more dust

K&N		95.6%			14.67 times more dust

Amsoil	98.5%			5 times more dust

Airaid		98.4%			5.33 times more dust